## Slide 1: YANG-2-Redis Transformer

## Slide 2: Purpose
Problem
  Every APP module must implement methods to convert YANG to REDIS schema and vice versa
Proposal
  Introduce generic transformer library to convert YANG to REDIS schema and vice versa using developer defined Transformer specification
  Skeleton transformer specification is auto-generated from YANG
  Generic APP module for standard cases – including data conversion, validation (via CVL), locking, and DB operations
  Extensions support to handle special cases or conversions
  Notifications support for gNMI, REST, and CLI
  Plug-in concept – existing APP modules can be updated to use plugin or continue with current approach

## Slide 3: Scope of Proof of Concept
  Showcase transformer spec, special transformer function portion of the transformer library.
  Supports only ACL Table and rules create request.
  Reuses the YGOT structure update and DB access layer calls from existing app module.
  Show case code reduction on the translation function, by using the transformer spec.

## Slide 4
Design: TransLib

## Slide 5: Overview Transformer Library
The transformer library provides standard infrastructure for transformation, validation and configuration.
The transformer spec can be used to programmatically define the rules on how to translate between heterogeneous data models in simple JSON.
Transformation Specification Defines translation between YANG path based dataset to REDIS schema and vice versa
Transformer class:
  Built-in default transformer methods can support simple translation.
  Transformer methods can be overloaded by developer to perform complex translation.
Notification spec (for unsolicited message): to define the observed tables/fields, test and notify the events to subscribed clients like REST server.
Notifier class: default notifier, subscribe method
Transformer spec can be extended by introducing a new JSON notation(e.g. to support db/table watchkeys, non-db data provider api etc).

## Slide 6
Example 1: Transformer Spec: Simple case
Using Transformer Spec:
{
" MODULE-NAME ": "sonic",
" PREFIX-NAME ": "so",
" TRANSFORM-SPEC ": {
" YOBJECTS ": [
{ " YOBJECT": "config
"YCHILDOBJECTS": [
{ " YOBJECT ": "vrouter",
" TABLE-NAME ": "VNET",
" KEY ": {
" YLEAFY ": [ "vnet-id“
]
},
" FIELDS": [ {
" YLEAFY ": "vni",
" FIELD-NAME ": "MYvni"
},
{
" YLEAFY ": "vxlan-tunnel"
} ]
} ]
}
}
Input Yang json:
{ "sonic:config": {
"vrouter" : [
{ "vnet-id" : "Vnet1", "vni": 1000, "vxlan-tunnel" : "tunnel_v4"
} ]
}
}
Output DB json:
{
"VNET": {
"Vnet1": {
“MYvni": "1000",
"vxlan_tunnel": "tunnel_v4“
}
}
}
Yang data from app-interface to transformer
DB data from transformer to app-interface after converstion

## Slide 7: Example 2: Transformer Spec: special transformer function case
Using Transformer Spec:
"MODULE-NAME": "openconfig-acl",
"PREFIX-NAME": "op-acl",
"TRANSFORM-SPEC": {
"YOBJECTS": [ {
"YOBJECT": "acl",
"YCHILDOBJECTS": [ {
"YOBJECT": "acl-sets",
"YCHILDOBJECTS": [ {
"YOBJECT": "acl-set",
"TABLE-NAME": "ACL_TABLE",
"KEY": {
"YLEAFY": [
"name",
"type"
],
"TRANSFORMER": "xfmr_acl_table_key"
}
"YCHILDOBJECTS": [ {
"YOBJECT": "config",
"FIELDS": [ {
"YLEAFY": [
"description"
],
"FIELD-NAME": "policy_desc"
},
{
"YLEAFY": [
"type"
]
}
]
}
}
}
Input Yang json:
{
"acl-sets": {
"acl-set": [ {
"name": "MyACL1",
"type": "ACL_IPV4",
"config": {
"name": "MyACL1",
"type": "ACL_IPV4",
"description": "Description for MyACL1"
}
}
]
}
}
Output DB json: {
"ACL_TABLE": {
"MyACL1_ACL_IPV4": {
"type": "L3",
"policy_desc": "Description for MyACL1",
}
}
}
Yang data from app-interface to transformer
DB data from transformer to app-interface after converstion

## Slide 8: Developer Workflow
Without transformer
Implement feature YANG and generate YGOT bindings.
Simple case:
Implement the translib library app interface (app module)
  Write conversion routines to translate between YANG schema to REDIS schema and vice versa
  Invoke the db access layer for validation and configuration
  Special function case:
Implement the translib library app interface (app module)
  Write conversion routines to translate between YANG schema to REDIS schema and vice versa
  Invoke the db access layer for validation and configuration
With transformer
Implement feature YANG and generate YGOT bindings.
Simple case:
Generate skeleton transformer-spec from YANG.
Update transformer-spec with REDIS table mapping.
  Special function case:
Generate skeleton transformer-spec from YANG.
Update transformer-spec with REDIS table mapping.
Write transformer function for special handling cases.

## Slide 9: Benefits
Transformer library infra code will take care of data conversion, validation (via CVL), locking, and DB operations.
No coding is required for simple case(one to one mapping between yang and redis schema).
Common transformer functions can be reused across app modules.
Only fields requiring special handling, require specific transformer handling functions.
Evaluating multiple language option support, for transformer functions.
Simplifies developer effort and reduces possibility of introducing bugs.
Diff on acl_app.go with the introduction of transformer library. https://github.com/project-arlo/sonic-mgmt-framework/commit/7bf80422eecbd012e48b5286019d813e76ad5a3d#diff-96fd08d6059562c8b508db1d1002a5f7L1065

## Slide 10: Backup

## Slide 11
Transformer spec
.
.
.
.
.
.
transformer-lib
openconfig-specs
openconfig-acl
acl_spec.json
xfmr
openconfig-system
system_spec.json
Yang to Spec generator
Openconfig Yang
Transformer Spec
Redis DB map info
spec creation
Generate transformer-spec from openconfig yang.
Input redis-db mapping details in the transformer-spec.
Create a directory for openconfig yang module in transformer-lib dir and place the transformer-spec & user defined handlers in it.

## Slide 12
APP
Transformer
Init (Yang to DB spec module): Load transformer-specs of all openconfig yang models and create lookup table with yang to redis-db mapping.
NBI request
Yang data (json)
Data converstion:
Interface to app: receives yang data from apps.
Yang to DB converter:
* Table lookup to get redis db info.
* Interact with app-specific db data modifiers(transformers) if needed.
* Convert yang to redis-db data.
DB data (json)
Interface to app
Yang to DB converter
App specific DB data modifiers(xfmr)
Yang to DB Spec Module
Transformer
Spec
App 1
App N
Transformer
Transformer in-detail
App developer input
Transformer infra

## Slide 13
Yang | If the REDIS DB field mapping criteria is … | Then developer input to transformer-spec is …
root | - | table name
leaf | same as yang leaf | None
 | different from yang leaf name | field name
 | requires user defined handling | transformer function name in spec and corresponding function handler
 | same table as parent object | None
 | different table than the parent object | table name
key | one yang leaf | None
 | multiple yang leaves with default delimiters | None
 | one or more yang leaves requiring user defined handling | transformer function name in spec and corresponding function handler
object (container/list) | same member fields as yang | None
 | requires user defined handling | transformer function name in spec and corresponding function handler
 | different table than the parent object | table name
Transformer Spec: Developer quick reference