## Slide 1: Build limitless network with Smart Switch
Introduction to Smart Switch in Data Centers

## Slide 2: Build limitless network with Smart Switch
Networking
Lihua Yuan, VP Engineering, Microsoft
Guohan Lu, Partner Software Engineer, Microsoft
Prince Sunny, Principal Software Engineer, Microsoft
NETWORKING

## Slide 3: Smart Switch - Hardware Concept
2RU Switch
Switching
  32 x 400G port Switching ASIC
  28 x 400G Front Panel
  8 x 200G or 4 x 400G to DPU/IPUs
DPU
  8 x DPUs
Control Plane
  128GB RAM
BO - Content
12.8T ASIC
4x400G/8x200G
DPU
DPU
DPU

## Slide 4: Smart Switch - Motivation
Why Smart Switch as compared to SmartNIC?
  Resource Pooling - SmartSwitch is augmenting the SmartNIC capability, enabling cloud providers to leverage SmartSwitch for highly scalable resource allocation and utilizing the NPU capabilities for High Availability and packet redirections.
  Powerful - SmartSwitch that accommodates a powerful NPU and highly scalable, high memory DPUs enable building limitless network by providing a powerful resource pool. DPUs are programmable to fit custom pipeline and can be used for offloading Internet routes, SDN policies to name a few.
  Speed and Reliability - SmartSwitch provides an in-band packet processing solution without any bounce back, thus reducing additional latencies. For SmartNIC deployment, the packets first lands on the SmartNIC, does the processing and then forwarded to VM. This flow can cross cluster boundaries. By having SmartSwitch in the same cluster as the VMs, there are no additional hops and network functions can be applied in the same path as to VM.
  Cost Savings - SmartSwitch provides a solution that does not require additional space within a datacenter. Also enabling savings on power usage and overall cost of product.
BO - Content

## Slide 5: Smart Switch – Placement proposal
T2-1-1
T2-1-2
T2-1-8
T3-1
T3-2
T3-3
T3-4
Tier 1 – MoR
T2-4-1
T2-4-2
T2-4-4
Tier 2 - Spine
T1-1
T1-8
T1-7
…
T1-2
…
…
Tier 3 - Regional Hub
…
T1-1
T1-8
T1-7
…
T1-2
T1-1
T1-8
T1-7
…
T1-2
Tier 0/ToR - Rack
…
T0-1
T0-2
T0-20
Servers
…
T0-1
T0-2
T0-20
…
T0-1
T0-2
T0-20
SONIC
SONIC
SONIC
SONIC
SONIC
SONIC
SONIC
SONIC
SONIC
SONIC
SONIC
SONIC
SONIC
SONIC
SONIC
SONIC
SONIC
SONIC
SONIC
SONIC
SONIC
Servers
Servers
Server or Appliance
Smart Switch
Smart Switch T1
Smart Switch ToR
Notes: Can live on any tier Representative diagram
https://github.com/sonic-net/DASH/blob/main/documentation/general/dash-high-level-design.md#example-of-network-representation

## Slide 6: Smart Switch - Use Case - Powered by DASH
TOR
TOR
Smart Switch
DASH
DPUs
FPGA/ASIC
FPGA/ASIC
SDN policies evaluation
Hyper-V Switch
VFP
Hyper-V Switch
VFP
Offload SDN policies evaluation to disaggregated switch/appliance
Lower power, lower latency
Higher throughput and IO
Notes: This is the problem we are trying to solve. Disaggregate the DPUs from the host.
Pulled them into an appliance or switch (pooling / disaggregating).
We tunnel VXLan from the VM to the Appliance/Switch for policy management.
10’s of M of CPS to keep up with demands of the VMs

## Slide 7: Smart Switch – High Availability
What is HA?
  Enabling a Single SmartSwitch or DPU going down not causing interruption or traffic impact to the service hosted on the DPUs
  Achieved by programming policies across the HA pair (Active/Standby or Active/Active) and performing Flow-Sync
  SmartSwitch NPUs can detect DPU failures in fraction of a second, using BFD or similar keep-alive mechanism, thus redirecting traffic to peer DPU.
HA Goals
Notes: This is the problem we are trying to solve. Disaggregate the DPUs from the host.
Pulled them into an appliance or switch (pooling / disaggregating).
We tunnel VXLan from the VM to the Appliance/Switch for policy management.
10’s of M of CPS to keep up with demands of the VMs

## Slide 8: Smart Switch – High Availability
Flow-Sync
  Active/Standby resource allocation on two DPUs from two different SmartSwitch forming HA pair
  One DPU serves as active and making flow decisions, while the other DPU serves as standby, only accepting flows from active.
  In steady state, all flows shall be inline sync-ed from active to standby. When a DPU joins the HA pair, initiate flow bulk-sync
  During active DPU failover, switchover from standby to new active
Notes: This is the problem we are trying to solve. Disaggregate the DPUs from the host.
Pulled them into an appliance or switch (pooling / disaggregating).
We tunnel VXLan from the VM to the Appliance/Switch for policy management.
10’s of M of CPS to keep up with demands of the VMs

## Slide 9: Smart Switch – High Availability
Smart Switch deployed as Tier–1 Switches
When a T1 NPU receives a packet destined to a resource allocated on a DPU, it forwards the packet to the active DPU using a Vxlan tunnel.

## Slide 10: Smart Switch – High Availability
In the diagram below, DPUs are running ENI workloads (ENIs are representations of VMs)
Leveraging Card-level ENI pairing

## Slide 11: Smart Switch – High Availability
Active/Standby per ENI
NPU encaps all traffic for an ENI to the DPU hosting the active ENI

## Slide 12: Smart Switch – NPU Requirements
Decap vxlan packet (Optional Decap if Dst IP is NPU loopback)
ACL Match Capabilities and Redirect to local or remote DPU
Encap with Vxlan
HW offloaded BFD to monitor remote and local DPUs

## Slide 13: Smart Switch – Software Architecture on SONiC

## Slide 14: Smart Switch – Extending SONiC/SAI to support DPU

## Slide 15: Acknowledgments
Dave Maltz | Technical Fellow, CVP
Deepak Bansal | Technical Fellow, CVP
Lihua Yuan | VP Engineering
Rishab Tiwari | Partner Software Engineer
Guohan Lu | Partner Software Engineer
Xin Liu | Principal Program Manager
Yanzhao Zhang | Principal TPM
Gerald Grace | Principal TPM Manager
Kristina Moore | Principal TPM Manager
Michal Zygmunt | Principal Software Engineer​
Avijit Gupta | Principal Software Engineer​
Sushant Sharma | Principal Software Engineer​
Pranjal Shrivastava | Principal Software Engineer​
Neeraj Motwani | Principal Software Engineer​
Abhijeet Kumar | Principal Software Engineer
Riff Jiang | Principal Software Engineer
Prince Sunny | Principal Software Engineer
& Smart Switch Working Group

## Slide 16: [Call to Action] [MANDATORY]
SmartSwitch forum - https://lists.sonicfoundation.dev/g/sonic-smartswitch
Inviting contributions for DASH SAI for more use-cases - Join sonic-dash@googlegroups.com
Timeline for Contribution by Dec’2023
Link to Contribution - https://github.com/sonic-net/SONiC/wiki/Becoming-a-contributor
Where to find additional information (URL links)
https://lists.sonicfoundation.dev/g/sonic-smartswitch/topics
Calendar: https://lists.sonicfoundation.dev/g/sonic-smartswitch/calendar
Mailing list: https://lists.sonicfoundation.dev/g/sonic-dev
BO - Content