## Slide 1: SONiC PON HLD Summary
Passive Optical Network for Datacenter OOB Management
https://github.com/sonic-net/SONiC/pull/2377

## Slide 2: Brief Overview of PON
PON Network
SONiC Router
PON | Passive Optical Network
OLT | Optical Line Terminal — the PON head-end device managed by this feature.
OLT Interface | An optical interface associated with an OLT, which is connected to a set of downstream ONUs.
OLT Plug | aka micro OLT (uOLT) — a small form factor optical plug that combines the OLT function and the OLT interface into one device.
ONU | Optical Network Unit — a PON subscriber-side endpoint.
Managed devices
Forwarding Plane
OLT
ONU
ONU
…
ONU
uni
uni
uni
uni
uni
uni
nni
nni
nni
PON Control Plane
The PON control plane interacts
with PON components through various
protocols such as ONU Management
and Control Interface (OMCI). These
may need to be trapped to/from the router
hardware forwarding plane.

## Slide 3: SONiC PON Integration – High-Level Architecture
SWSS
CONF_DB
Rest of SONiC
PON models
STATE_DB
monitoring systems
APPL_DB
ponmgrd
docker-pon-manager
PON_ASIC_DB
orchagent
PonOrch
dcpon-syncd
sai_pon_api_t
PON_COUNTERS_DB
ponprotd
Dual-Homed PON Gateway
Vendor SDK
dcsai poll
dcsai crud
docker-pon-syncd
Vendor stack
gNMI
state xpaths
state alarms
stat xpaths
new SONiC process
existing SONiC process
new SONiC container
new SONiC API/model/code
new vendor component
stats alarms
PON_FLEX_COUNTER_DB

## Slide 4: Architectural Goals
Introduce PON capabilities with no impact on non-PON deployments
  Minimal changes to existing code
  Zero resource cost for deployments that don’t need PON
    Optional containers
    No system resources used unless PON enabled
Full PON – residential broadband, etc – includes a large feature set. This project aims to enable only the subset that’s relevant to datacenter applications, specifically out of band management networks for GPUs, servers, and other infrastructure.
Note on scaling: PON topologies scale in the number of OLT interfaces and the number of ONUs per interface.
  There are various tradeoffs involved (fiber plant size, splitter density, TDM versus bandwidth, etc).
  The specific scaling behavior of any given platform will depend on the deployment requirements for that platform.
  As an example, current realistic deployment models use 36-48 OLT interfaces, with 76-128 ONUs per OLT interface.
  The platform’s compute capacity will need to be sized accordingly – this is a vendor or system design constraint.

## Slide 5: Container: docker-pon-manager
Houses ponmgrd which handles CONF_DB -> APPL_DB. Vendor agnostic.
  All new tables – no modifications to existing tables. Table prefix PON_* (PON_CONTROLLER, PON_OLT_INTF, etc)
Also houses ponprotd, which handles the Dual Homed PON Gateway function – details for this are covered by another HLD

## Slide 6: PonOrch
Orch subclass responsible for APPL_DB -> sairedis interaction for APPL_DB PON_* tables
This code will reside in SWSS along side other orch components, dormant outside of PON deployments
Vendor agnostic
  Will use sai_query_attribute_capability() to determine which optional or vendor-specific SAI attributes are supported

## Slide 7: Container: docker-pon-syncd
Houses dcpon-syncd
  Similar to gearbox – this is a separate instance of the syncd binary, dedicated to the PON HW interaction
Loads vendor-specific PON SAI extension library
Consumes sai-redis from PON_ASIC_DB
Maintains flex counters in PON_COUNTERS_DB and PON_FLEX_COUNTER_DB
Will use subclasses and other existing extension mechanisms to incorporate PON-specific behaviors – dormant outside of PON deployments

## Slide 8: High Level Container and Deployment Architecture
PON functionality will be encapsulated in the two new PON containers
The docker-pon-manager container is vendor agnostic
The docker-pon-syncd container is vendor specific, populated with the vendor SAI SDK extension at build time
The lifecycles of these two containers are coupled – they are only launched on deployments that require them (see next slide)

## Slide 9: A Note About Hardware Architecture
Some hardware platforms will include an OLT on the platform directly. These platforms can select vendor SAI SDK based on SKU/platform, in the same way ASIC SAI SDKs are loaded.
Other hardware platforms may not have native OLTs built into the SKU – these can still use micro-OLT (uOLT) to implement PON functionality
  In this case the decision to launch the PON containers, and the decision as to which SAI SDK to load, may need to be config driven

## Slide 10: Container Launch Logic
PLATFORM=$(sonic-cfggen -H -v DEVICE_METADATA.localhost.platform)
CONFIGFILE="/usr/share/sonic/device/${PLATFORM}/dcponsyncd.ini"
if CONFIGFILE exists:
use CONFIGFILE contents to determine how to start the container pair
(i.e. which vendor-specific docker-pon-syncd image to use)
else:
use sonic-cfggen to check CONFIG_DB for keys that indicate the
container pair should be started; specific keys or key values may
also select a vendor-specific docker-pon-syncd variant

## Slide 11: Data Model
The SONiC PON data model will be based on a subset of broadband forum’s TR-385 Yang model
  Residential broadband contains significant complexity – much of it is not needed for datacenter applications
  We are proposing to create a community SONiC model that maps, rather than trying to use TR-385 directly
  This is due to the depth and complexity of the TR-385 model – it has multi-level container structures that don’t translate readily to SONiC’s flatter table structure
PON still has a large configuration/operational model area even after removing non-datacenter functionality

## Slide 12: Notes on Redis DB
The PON architecture mimics gearbox in a few different ways
One of these is the use of a new logical Redis instance IDs for PON_ASIC_DB, PON_COUNTERS_DB, and PON_FLEX_COUNTER_DB, plus corresponding infrastructure changes to support them (context IDs, etc)
This is needed for the same reasons gearbox needs it – it allows PonOrch to manage the sai-redis interactions without interfering with the existing SWSS sai-redis instances

## Slide 13: CLI Examples
pon controller controller-name CNTL-1 device-id 4c:09:97:f0:75:36 olt-timeout 360
pon olt-intf olt-intf-name OLT-1 device-id 78:5f:a4:45:8b:9a pon-enable true port-id Ethernet16
show pon olt-intf OLT-1

## Slide 14: PON Counters
dcpon-syncd will implement flex counters for PON
  Due to potential large scale, ONUs will be partitioned into per-OLT-interface shards – the sharding and/or thread mapping will be determined by vendor via SAI: SAI_PON_OLT_INTF_ATTR_STATS_COLLECTION_CONCURRENCY
There are a large number of counters, so only 5 OLT tables and 2 ONU tables are proposed to be enabled by default – operators can enable additional counters using configured flex counter groups
The default intervals are 5 minutes for OLT, 15 minutes for ONU
Some counter sources are higher frequency and/or volume than others – platform capacity needs to be matched to PON scale

## Slide 15: ponutil
PON hardware has firmware management and action requirements
The proposal is to introduce a ‘ponutil’ command for this, similar to the ‘sfputil’ command
  Ponutil will manage firmware images (download, staging, activation) for uOLTs and ONUs
  It will provide action operations such as reset

## Slide 16: SAI
The PON SAI API will be an SAI experimental API
The proposal is for this API to mirror the Yang model more or less 1:1
  The API will be large – there are 86 configuration tables, 25 operational state tables, and 64 counter tables in the proposed Yang model, and most if not all the attributes there map onto the PON control plane and so must be mapped into the SAI API

## Slide 17: 1904.2 Frame Handling
The PON control plane protocols (OMCI, etc) are carried on IEEE 1904.2 frames.
These frames need to be injected/extracted on the router CPU
Because they are control frames, they will need appropriate CoS treatment so that they do not get dropped due to fast path congestion, etc
As part of the SAI submission, we will be proposing to leverage the COPP framework to trap these packets and direct them to the desired queue/policer.
This approach requires ASIC SAI vendors to add support to their SDK for this trap type.
In the interim, we are proposing to add code to PonOrch, gated on whether PON is deployed, that will check for the ASIC trap capability, and if it is not present, use existing SAI APIs to add a custom trap.

## Slide 18: Performance
Memory consumption
  No memory required unless PON is activated on the platform
  Per-container infrastructure for 2 new containers
  3 additional processes, baseline 50MB or less per process, plus per-object cache scaling for PON configuration
  Redis memory scales predominantly with ONUs (to a lesser extent with OLTs)
    Per ONU across all tables expected to be less than 1MB
    Per OLT across all tables expected to be less than 100KB
Redis load
  The bulk of the redis load will come from counters.
  With the default collections, OLTs need 5904 HSETs per cycle globally, 123 per shard if sharding 48 OLTs
  ONUs need 65K HSETs per cycle globally, 1368 per shard if sharding 48 OLTs